ANTENNA Q2344B2XL

DESCRIPTION:

| Boomlength | Number of elements | Diameter of elements | Height of elements | Antenna for very high gain and light construction, recommended material: silver |
| --- | --- | --- | --- | --- |
| 4250 mm | 44 | 1,5 mm | 19 mm |  |

PERFORMANCES:

| Element material | G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) | Bandwidth (MHz) for SWR=1,5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No loss | 21,96 | 24,23 | 21,22 | 20,56 | 16,0 | 16,2 | 12,9 | +10,86 | 1287,900-1299,950 |
| Aluminum rods | 21,82 | 24,18 | 21,28 | 20,62 | 16,0 | 16,2 | 22,0 | +8,39 |  |
| Silvered rods | 21,87 | 24,2 | 21,26 | 20,60 | 16,0 | 16,2 | 18,7 | +9,14 |  |

DIMENSIONS:

|  | Ref | De | D1 | D2 | D3 | D4 | D5 | D6 | D7 | D8 | D9 | D10 | D11 | D12 | D13 | D14 | D15 | D16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Pos | 0 | 50 | 73 | 113 | 162 | 230 | 308 | 399 | 499 | 602 | 705 | 813 | 920 | 1028 | 1137 | 1248 | 1353 | 1464 |
| Length | 104 | 95,5 | 93 | 87 | 86 | 84 | 82 | 80 | 78 | 77 | 76 | 75 | 74 | 73 | 73 | 73 | 72 | 72 |
|  | D17 | D18 | D19 | D20 | D21 | D22 | D23 | D24 | D25 | D26 | D27 | D28 | D29 | D30 | D31 | D32 | D33 | D34 |
| Pos | 1571 | 1683 | 1793 | 1903 | 2013 | 2118 | 2225 | 2316 | 2398 | 2497 | 2590 | 2721 | 2835 | 2939 | 3050 | 3161 | 3277 | 3380 |
| Length | 71 | 70 | 70 | 68 | 68 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 |
|  | D35 | D36 | D37 | D38 | D39 | D40 | D41 | D42 |  |  |  |  |  |  |  |  |  |  |
| Pos | 3493 | 3610 | 3715 | 3828 | 3939 | 4045 | 4160 | 4250 |  |  |  |  |  |  |  |  |  |  |
| Length | 66 | 66 | 66 | 66 | 66 | 66 | 66 | 66 |  |  |  |  |  |  |  |  |  |  |
| All measures given in milimeters |

DIAGRAMS

NO LOSS INCLUDED

LOSSES INCLUDED (aluminum)

LOSSES INCLUDED (silver)