| ANTENNA QY70805XL8D3 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 4 | 3 | 8 | 1165 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | DQ1 | DQ2 | DQ3 |
| Position | 0 | 54 | 104 | 141 | 254 | 472 | 708 | 959 | 1165 |
| Length | 335 | 354 | 282 | 309 | 306 | 293 | 175 | 171 | 165 |
| Remark | All elements made of Al tubes Ǿ5 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 13.61 | 25.89 | 19.54 | 15.67 | 40.0 | 44.0 | 39.4 | -1.96 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 13.56 | 3.4 | 39.4 | -2.36 | 420.800 – 438.500 |
| After KF2YN correction | 13.50 | 3.4 | 42.4 | -2.77 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance | 1140 |  | 1140 |
| Vertical distance |  | 880 | 880 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 880 | 16.34 | 38.7 | 3.4 | +0.46 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1140 | 16.54 | 42.7 | 3.4 | +0.24 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1140 | 19.42 | 39.5 | 3.4 | +3.46 |
| V = 880 |  |  |  |  |
| Four antennas in H-stack |