| ANTENNA QY70908XL4D2 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 2 | 9 | 1475 |
| DIMENSIONS |
|  | 0 | 50 | 110 | 155 | 274 | 474 | 719 | 978 | 1246 | 1475 |
| Position | 331 | 330 | 330 | 303 | 301 | 290 | 283 | 274.5 | 171 | 157 |
| Length | 0 | 50 | 110 | 154 | 277 | 481 | 719 | 981 | 1249 | 1475 |
| Remark | All elements made of Al tubes Ǿ8 mm The height of rectangles is 165 mm All dimensions given in milimetres |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 14.25 | 23.20 | 20.29 | 17.42 | 37.2 | 41.0 | 35.0 | -0.88 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 14.21 | 2.6 | 35.0 | -1.23 | 421.500 – 438.000 |
| After KF2YN correction | 14.21 | 2.6 | 37.3 | -1.50 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1280 | 1280 |
| Vertical distance | 940 |  | 940 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 940 | 17.04 | 34.9 | 2.6 | +1.61 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1280 | 17.22 | 37.8 | 2.6 | +1.45 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1280 | 20.11 | 36.1 | 2.6 | +3.54 |
| V = 940 |  |  |  |  |
| Four antennas in H-stack |