| ANTENNA QY71405XL7D7 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 7 | 14 | 2925 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 | DQ2 | DQ3 | DQ4 | DQ5 | DQ6 | DQ7 |
| Position | 0 | 60 | 100 | 129 | 230 | 418 | 652 | 909 | 1196 | 1481 | 1788 | 2093 | 2386 | 2688 | 2925 |
| Length | 335 | 342 | 292 | 303 | 309 | 298 | 291 | 284 | 166 | 158 | 151 | 149 | 147 | 145 | 141 |
| Remark | All elements made of Al tubes Ǿ5 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 16.26 | 27.96 | 22.57 | 18.71 | 31.2 | 32.8 | 26.0 | +2.90 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 16.20 | 4.0 | 26.0 | +2.15 | 426.000 – 439.800 |
| After KF2YN correction | 16.13 | 4.0 | 29.6 | +1.41 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1540 | 1540 |
| Vertical distance | 1680 |  | 1680 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1680 | 19.22 | 28.6 | 4.0 | +4.66 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1540 | 19.16 | 29.3 | 4.0 | +4.49 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1540 | 22.23 | 29.1 | 4.0 | +7.60 |
| V = 1680 |  |  |  |  |
| Four antennas in H-stack |