| ANTENNA QY71606XL4D9 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 9 | 16 | 3525 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 |
| Position | 0 | 65 | 100 | 133 | 236 | 421 | 649 | 906 | 1182 |
| Length | 335 | 350 | 296 | 304 | 307 | 298 | 290.5 | 283.5 | 171 |
|  | DQ2 | DQ3 | DQ4 | DQ5 | DQ6 | DQ7 | DQ8 | DQ9 |  |
| Position | 1456 | 1754 | 2058 | 2364 | 2672 | 2974 | 3276 | 3525 |  |
| Length | 163 | 157 | 153 | 150 | 146 | 143 | 141 | 139 |  |

| Remark | All elements made of Al tubes Ǿ6 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| --- | --- |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 17.10 | 35.36 | 23.95 | 19.87 | 28.6 | 29.6 | 24.9 | +4.01 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 17.04 | 4.6 | 24.9 | +3.19 | 422.500 – 439.000 |
| After KF2YN correction | 16.95 | 4.6 | 29.1 | +2.32 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1780 | 1780 |
| Vertical distance | 1780 |  | 1780 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1780 | 20.03 | 28.0 | 4.6 | +5.56 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1780 | 20.00 | 28.6 | 4.6 | +5.44 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1780 | 23.07 | 27.7 | 4.6 | +8.65 |
| V = 1780 |  |  |  |  |
| Four antennas in H-stack |