| ANTENNA QY71610XL3D9 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 9 | 16 | 3525 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 |
| Position | 0 | 54 | 91 | 135 | 235 | 424 | 654 | 916 | 1196 |
| Length | 331 | 343 | 343 | 302 | 300.5 | 289 | 281 | 272 | 169 |
|  | DQ2 | DQ3 | DQ4 | DQ5 | DQ6 | DQ7 | DQ8 | DQ9 |  |
| Position | 1468 | 1788 | 2076 | 2392 | 2692 | 2986 | 3225 | 3525 |  |
| Length | 159 | 153 | 151 | 149 | 147 | 147 | 147 | 143 |  |

| Remark | All elements made of Al tubes Ǿ10 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| --- | --- |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 17.26 | 29.36 | 21.07 | 17.47 | 27.6 | 28.4 | 27.2 | +3.33 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 17.22 | 2.9 | 27.3 | +2.86 | 423.000 – 438.500 |
| After KF2YN correction | 17.17 | 2.9 | 29.8 | +2.43 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1720 | 1720 |
| Vertical distance | 1780 |  | 1780 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1780 | 20.26 | 27.9 | 2.9 | +5.80 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1720 | 20.21 | 28.9 | 2.9 | +5.60 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1720 | 23.29 | 27.4 | 2.9 | +8.91 |
| V = 1780 |  |  |  |  |
| Four antennas in H-stack |