| ANTENNA QY71708XL5D10 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 10 | 17 | 3825 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 |
| Position | 0 | 61 | 93 | 130 | 230 | 421 | 654 | 916 | 1186 |
| Length | 333 | 353 | 288 | 303.5 | 305 | 294 | 286 | 279 | 170 |
|  | DQ2 | DQ3 | DQ4 | DQ5 | DQ6 | DQ7 | DQ8 | DQ9 | DQ10 |
| Position | 1474 | 1774 | 2062 | 2388 | 2682 | 2982 | 3286 | 3582 | 3825 |
| Length | 162 | 158 | 154 | 152 | 150 | 147 | 145 | 143 | 140 |

| Remark | All elements made of Al tubes Ǿ8 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| --- | --- |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 17.59 | 30.91 | 22.02 | 18.15 | 26.8 | 27.4 | 25.8 | +4.53 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 17.53 | 3.7 | 25.8 | +3.76 | 425.400 – 437.400 |
| After KF2YN correction | 17.44 | 3.7 | 29.2 | +2.80 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1800 | 1800 |
| Vertical distance | 1800 |  | 1800 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1800 | 20.51 | 27.5 | 3.7 | +6.12 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1800 | 20.49 | 28.5 | 3.7 | +5.95 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1800 | 23.56 | 27.0 | 3.7 | +9.25 |
| V = 1800 |  |  |  |  |
| Four antennas in H-stack |