| ANTENNA QY72206XL1D15 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 15 | 22 | 5325 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 | DQ2 | DQ3 | DQ4 |
| Position | 0 | 65 | 100 | 131 | 233 | 419 | 648 | 905 | 1182 | 1456 | 1754 | 2058 |
| Length | 336 | 349 | 304 | 304 | 307.5 | 298 | 291.5 | 283.5 | 171 | 163 | 159 | 155 |
|  | DQ5 | DQ6 | DQ7 | DQ8 | DQ9 | DQ10 | DQ11 | DQ12 | DQ13 | DQ14 | DQ15 |  |
| Position | 2364 | 2672 | 2974 | 3272 | 3589 | 3878 | 4192 | 4478 | 4782 | 5084 | 5325 |  |
| Length | 151 | 149 | 147 | 145 | 145 | 141 | 141 | 141 | 135 | 135 | 135 |  |

| Remark | All elements made of Al tubes Ǿ6 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| --- | --- |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 18.48 | 42.92 | 21.67 | 18.32 | 24.6 | 25.0 | 24.4 | +5.46 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 18.51 | 4.3 | 24.1 | +5.06 | 421.500 – 438.500 |
| After KF2YN correction | 18.35 | 4.3 | 28.3 | +3.83 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1980 | 1980 |
| Vertical distance | 2000 |  | 2000 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1980 | 21.40 | 27.4 | 4.3 | +7.01 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 2000 | 21.39 | 28.0 | 4.3 | +6.91 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 2000 | 24.45 | 27.5 | 4.3 | +10.05 |
| V = 1980 |  |  |  |  |
| Four antennas in H-stack |