| ANTENNA QY72308XL4D16 |
| --- |
| DESCRIPTION |
| Radiator | Number of yagi elements | Number of oblong elements | Total number of elements | Boomlength (mm) |
| LFA | 6 | 16 | 23 | 5595 |
| DIMENSIONS |
|  | Ref | De1 | De2 | D1 | D2 | D3 | D4 | D5 | DQ1 | DQ2 | DQ3 | DQ4 |
| Position | 0 | 45 | 97 | 128 | 220 | 406 | 626 | 886 | 1161 | 1439 | 1729 | 2034 |
| Length | 331 | 331 | 331 | 303 | 305 | 294 | 287 | 278.5 | 170 | 164 | 158 | 153 |
|  | DQ5 | DQ6 | DQ7 | DQ8 | DQ9 | DQ10 | DQ11 | DQ12 | DQ13 | DQ14 | DQ15 | DQ16 |
| Position | 2351 | 2634 | 2932 | 3205 | 3506 | 3792 | 4114 | 4402 | 4712 | 5048 | 5318 | 5595 |
| Length | 151 | 150 | 149 | 147 | 145 | 143 | 143 | 143 | 141 | 141 | 141 | 139 |

| Remark | All elements made of Al tubes Ǿ8 mm The height of rectangles is 170 mm All dimensions given in milimetres |
| --- | --- |
| PERFORMANCES (No loss condition) |
| G (dBi) | F/B (dB) | F/Sh (dBi) | F/Sv (dBi) | Hor (◦) | Ver (◦) | Temp (◦K) | G/T (dB) |
| 19.03 | 30.47 | 19.96 | 17.53 | 22.6 | 22.8 | 25.7 | +5.39 |
| DIAGRAMS |
| Horizontal and verticall pattern in free space, no loss condition |
| PERFORMANCES (Loss included for aluminum) |
| Aluminum | G (dBi) | Tloss (K) | TA (◦K) | G/T (dB) | Bandwidth for SWR=1.5 (MHz) |
| After NEC/EZNEC | 18.96 | 4.6 | 25.7 | +4.60 | 423.000 – 437.300 |
| After KF2YN correction | 18.92 | 4.6 | 29.9 | +4.16 |  |
| Remark: Red coloured data are the final antenna data, which means: KF2YN correction formula applied and loss for aluminum included |
| DIAGRAMS |
| Frequency diagram for SWR better than 1.5 |
| SWR diagram for the range from 432.000 – 435.000 MHz |
| Horizontal and vertical pattern in free space, loss included for aluminum |
| STACKING (ALL DATA GIVEN IN ACCORDANCE WITH KF2YN CORRECTION, LOSS INCLUDED) |
| RECOMMENDED STACKING DISTANCES |
|  | Two antennas vertically (mm) | Two antennas horizontally (mm) | Four antennas in H-stack (mm) |
| Horizontal distance |  | 1980 | 1980 |
| Vertical distance | 1840 |  | 1840 |
| TWO ANTENNAS STACKED VERTICALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1840 | 21.88 | 28.7 | 4.6 | +7.30 |
| Two antennas stacked vertically |
| TWO ANTENNAS STACKED HORIZONTALLY |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| 1980 | 21.98 | 29.8 | 4.6 | +7.24 |
| Two antennas stacked horizontally |
| FOUR ANTENNAS IN H-STACK |
| DISTANCE (mm) | G (dBi) | TA (K) | Tloss (K) | G/T (dB) |
| H = 1980 | 24.94 | 28.4 | 4.6 | +10.40 |
| V = 1840 |  |  |  |  |
| Four antennas in H-stack |